#include <lpc2000/io.h>

volatile int dummy;

const int delay = 100000;

int main(void) {

int i;

IODIR0 = BIT10;

while (1) {

for (i=0; i<delay; i++) dummy=1;

IOPIN0 |=  BIT10;

for (i=0; i<delay; i++) dummy=1;

IOPIN0 &= ~BIT10;

}

}

#include <lpc2000/io.h>

int main(void) {

IODIR0 = BIT10;

while (1) {

T0TC  = 0;            /* zero the counter            */

T0MR0 = 2999999;      /* match register              */

T0MCR = BIT2;         /* stop on match               */

T0TCR = BIT0;         /* start timer0!               */

while (T0TCR & BIT0);

IOPIN0 |=  BIT10;

T0TC  = 0;            /* zero the counter            */

T0MR0 = 2999999;      /* match register              */

T0MCR = BIT2;         /* stop on match               */

T0TCR = BIT0;         /* start timer0!               */

while (T0TCR & BIT0);

IOPIN0 &= ~BIT10;

}

}

#include <lpc2000/io.h>

#include <lpc2000/interrupt.h>

void __attribute__ ((interrupt("FIQ"))) fiq_isr(void) {

T0IR = BIT0;          /* clear the interrupt flag   */

/* toggle the LED              */

if (IOPIN0 & BIT10) IOPIN0 &= ~BIT10;

else                IOPIN0 |=  BIT10;

}

int main(void) {

IODIR0 = BIT10;

T0MR0 = 2999999;      /* match register              */

T0MCR = BIT0 | BIT1;  /* reset & interrupt on MR0    */

T0TCR = BIT0;         /* start timer0!               */

VICIntSelect = BIT4;  /* TIMER0 is the FIQ           */

VICIntEnable = BIT4;  /* enable TIMER0 interrupts    */

enable_interrupts();

while (1) {

}

}

#include <lpc2000/io.h>

#include <lpc2000/interrupt.h>

void __attribute__ ((interrupt("FIQ"))) fiq_isr(void) {

EXTINT  = BIT1;       /* clear the interrupt flag    */

/* toggle the LED              */

if (IOPIN0 & BIT10) IOPIN0 &= ~BIT10;

else                IOPIN0 |=  BIT10;

}

int main(void) {

IODIR0 = BIT10;

PINSEL0 = BIT29;      /* select EINT1 for P0.14      */

EXTMODE = BIT1;       /* INT1 is edge sensitive      */

/* falling edge by default     */

EXTINT  = BIT1;       /* clear the interrupt flag    */

VICIntSelect = BIT15; /* EINT1 is the fast interrupt */

VICIntEnable = BIT15; /* enable EINT1                */

enable_interrupts();

while (1) {

}

}